## Slide 1: IPv6 at SUNY Geneseo
Rick Coloccia
Network Manager
SUNY Geneseo

## Slide 2: IPv6 Defined
Successor to IPv4
128 bit addresses
Improvements over IPv4:
  v4: ~4.3 billion addresses
  v6: 340 undecillion (2^128) addresses
  Stateless autoconfiguration
  Subnets generally standardized at 64 bits
  Integrated security and IPSec compatibility

## Slide 3: IPv6 Defined
Is not an extension or revision to IPv4, but an entirely separate protocol, i.e.. appletalk or ipx/spx
Runs entirely parallel to your existing IPv4 deployment
Is the solution to the IPv4 address shortage. The last /8 has been allocated. We truly will run out of addresses soon…

## Slide 4: IPv6 & IPv4 at Geneseo
IPv4: 137.238.0.0/16
  Subnets of various sizes
IPv6: 2620:0000:5080:0000:0000:0000:0000:0000/48
  Abbreviated as 2620:0:5080::/48
  Subnets are all /64’s
Annual fee of $1250 for the v6 address space
I2-given vs. purchased addresses
  route aggregation necessary because of larger addresses

## Slide 5: IPv6 & IPv4 at Geneseo
IPv4 Subnets:
  137.238.60.0/24 (256 hosts)
  137.238.40.0/22 (1024 hosts)
  137.238.16.0/21 (2048 hosts)
IPv6 Corresponding Subnets:
  2620:0:5080:60::/64 (2^64 hosts)
  2620:0:5080:40::/64 (2^64 hosts)
  2620:0:5080:16::/64 (2^64 hosts)

## Slide 6: IPv6 & IPv4 at Geneseo
Servers:
  Statically defined addresses
  IPv4: 137.238.1.16
  IPv6: 2620:0:5080:1::16
  This parallel keeps things manageable for IT
  Wasteful? Eh…

## Slide 7: IPv6 & IPv4 at Geneseo
Clients:
  Hosts send link-local router solicitation multicast requests for configuration parameters
  “Stateless address auto configuration”

## Slide 8: Supporting IPv6 in the Network
Layer 3 Switches/Routers
  Yes, these must support IPv6. Require it on your next refresh.
Layer 2 Switches?
  Don’t bother. These are truly clients on your network. You already own v4 address. Use those. Or, like Geneseo, you use private or 10-net address in this equipment.

## Slide 9: Supporting IPv6 in the Network
Network Core
  ipv6 route ::/0 2620:0:5080:3001::2
Network Gateway
  ipv6 route 2620:0:5080::/48 2620:0:5080:3009::1
  BGP to select the route out (I2/Commercial)

## Slide 10: Supporting IPv6 in the Network
  interface Vlan3002
  description ~VLAN 3002 - Administration
  ip dhcp relay information trusted
  ip address 137.238.43.254 255.255.252.0
  ip helper-address 137.238.1.16
  ip pim sparse-dense-mode
  ipv6 address 2620:0:5080:40::1/64
  ipv6 enable

## Slide 11: Supporting IPv6 in the Network
Firewalls, NAC Appliances, IPS
  Yes, these must support IPv6. Require it on your next refresh. Everyone is supporting it now.
  At Geneseo:
    Our Firewall (Cisco ASA) fully supports and manages IPv6 traffic.
    Our IPS polices IPv6 traffic just as it does IPv4 traffic.
    Your VPN devices may need to support IPv6 as well. (Cisco Live! example)

## Slide 12: IPv6 in Servers: DNS
You’ll need to add AAAA DNS records for servers that you wish to be reachable over the Internet via your IPv6 address space. Easy.
Reverse DNS records can be added for static IPv6 addresses, but because of auto configuration, which is based on a derivative of the Ethernet address, reverse DNS isn’t done.

## Slide 13: IPv6 in Servers: Everything Else
Almost all servers and services work just fine now!
address-per-service, address-per-client
Old issues that have gone away:
  Apple OSX Server Management Tool
  Oracle – older versions
Portable devices

## Slide 14: Issues and Troubleshooting
Protocol failover
  arin.net example
Turn it off on the server having problems. 
IPv6 is evolving. Application support is strong but not 100%. The only way to “get it right” is to start running it now, so that when we need to rely on it we’re ready.

## Slide 15: Q & A?
Thanks for staying, travel home safely!
Rick Coloccia
coloccia@geneseo.edu